## Slide 1
Bansilal Ramnath Agarwal Charitable Trust’s
Vishwakarma Institute of Information Technology
Department of Electronics & Telecommunication
Project Phase – I , Presentation on “SWARMING OF DRONES”
(SPONSORED BY: DRDO)
(Domain : Robotics and IoT)
By : Group No. – A03
Under Guidance of MR. VISHAL AMBHORE
Year
2019-2020
Roll No. | Division | Name | Contact No.
411037 | A | Rushikesh Gamare | 7020260394
411038 | A | Kunal Gandhi | 8208859454
411062 | A | Amey Kore | 9404736709

## Slide 2: PROJECT PHASE – I, outline
Bansilal Ramnath Agarwal Charitable Trust’s
Vishwakarma Institute of Information Technology
Department of Electronics & Telecommunication
Introduction to Project
Component selection and software used
Result analysis and discussion
Application
References

## Slide 3: INTRODUCTION
Bansilal Ramnath Agarwal Charitable Trust’s
Vishwakarma Institute of Information Technology
Department of Electronics & Telecommunication
What is Swarm? Why Swarm?
Swarm robotics is an approach to the coordination of multiple robots as a system which consist of large numbers of mostly simple physical robots. This approach emerged on the field of artificial swarm intelligence, as well as the biological studies of insects, ants and other fields in nature, where swarm behavior occurs.
Large number of simple robots can perform complex tasks in a more efficient way than a single robot, giving robustness and flexibility to the group.
To increase work efficiency by communicating with one another.

## Slide 4: Component list
Bansilal Ramnath Agarwal Charitable Trust’s
Vishwakarma Institute of Information Technology
Department of Electronics & Telecommunication
Chassis
BLDC motor
Propeller
Landing gears
ESC
Flight controller
Power management board
Battery
GPS module
Receiver
Telemetry radio

## Slide 5: BLOCK diagram
Bansilal Ramnath Agarwal Charitable Trust’s
Vishwakarma Institute of Information Technology
Department of Electronics & Telecommunication
Basic UAV block diagram with peripherals

## Slide 6: 6(a).Hardware description
Bansilal Ramnath Agarwal Charitable Trust’s
Vishwakarma Institute of Information Technology
Department of Electronics & Telecommunication
Chassis F450 chassis (selected)
Weight- 282g
BLDC motor 1800kv rpm(selected)
Max rpm at 12v – 21600
Weight – 48g
No load current - 0.5A
No load voltage – 10v
Thrust generated with 3s battery and 1045 propeller – 1.2kg

## Slide 7
Bansilal Ramnath Agarwal Charitable Trust’s
Vishwakarma Institute of Information Technology
Department of Electronics & Telecommunication
ESC 20A hobbyking (selected) PWM frequency – 8k Hz to 16k Hz
Flight controller PIXHAWK4(selected)
2mb flash memory (ROM)
512 mb RAM
Main soc microcontroller in px4 – STM32F427
Failsafe soc – STM32F100
Power management board Input – 12v to 30v
Output – 12v ,5v PWM

## Slide 8
Bansilal Ramnath Agarwal Charitable Trust’s
Vishwakarma Institute of Information Technology
Department of Electronics & Telecommunication
Battery 3s LiPo 3000 MAh
Min voltage- 10.2 V
Nominal voltage – 11.1 V
Max voltage – 12.6 V
Receiver – X8R 16 channel duplex communication
operating frequency - 2.4 GHZ
Operating voltage – 4v to 10v
Output voltage – 3.3 V Operating current – 100 mA at 5 V
Max range – 1.5 km
Telemetry radio – 433Mhz Range – 3 km
Operating voltage – 3 V to 6 V

## Slide 9
Odroid microprocessor Odroid XU4
USB ports – 3
RAM – 2 GB
Input voltage – 5 V
Input current – 4A
8 GB eMMC5.0 HS400 flash storage Operating system - Ubuntu 16.04
Power supply for odroid – 5v, 4A buck converter
5v,4A lps for testing(using LM350),MJE2955

## Slide 10: BLOCK dIAGRAM
Bansilal Ramnath Agarwal Charitable Trust’s
Vishwakarma Institute of Information Technology
Department of Electronics & Telecommunication
 Denotes communication through UDP.

## Slide 11: Result analysis and discussion
Bansilal Ramnath Agarwal Charitable Trust’s
Vishwakarma Institute of Information Technology
Department of Electronics & Telecommunication
24 main GPS satellites orbit Earth every 12 hours, sending a synchronized signal from each individual satellite. Because the satellites are moving in different directions, a user on the ground receives the signals at slightly different times. When at least four satellites get in touch with the receiver, the receiver can calculate where the user is – often to a precision of just a few feet, for civilian use.

## Slide 12: Result analysis and discussion
Bansilal Ramnath Agarwal Charitable Trust’s
Vishwakarma Institute of Information Technology
Department of Electronics & Telecommunication
This is the log collected of the voltage of the battery during a single flight plan.It Shows the variation in the voltage supplied by the Battery to the system.

## Slide 13
Bansilal Ramnath Agarwal Charitable Trust’s
Vishwakarma Institute of Information Technology
Department of Electronics & Telecommunication
6(b).Required Software
Q ground controller
QGroundControl provides full flight control and mission planning for any MAVLink enabled UAV. Its primary goal is ease of use for professional users and developers. All the codes are open-source source, so you can contribute and evolve it as you want.
ArduPiolet
ArduPilot is an open source, unmanned vehicle Autopilot Software Suite, capable of controlling autonomous: Multi UAV’s, Ground rovers, Boats, Submarines.

## Slide 14: MAVLink(Micro Air Vehicle Link)
Bansilal Ramnath Agarwal Charitable Trust’s
Vishwakarma Institute of Information Technology
Department of Electronics & Telecommunication
What is MAVlink?
  Protocol for communicating with UAV’s.
  It follows modern hybrid publisher-subscriber protocol.
  UAV’s and central controlling unit connected each other by peer-to-peer network.
  Peer-to-peer network shown below.
  It mostly use to communicate within GCS and UAV’s.

## Slide 15: Key Features of MAVLink:
Bansilal Ramnath Agarwal Charitable Trust’s
Vishwakarma Institute of Information Technology
Department of Electronics & Telecommunication
Very efficient.
MAVLink 2 has just 14 bytes of overhead.
Not required any additional framing.
Very reliable.
It provides methods for detecting packet drops, corruption, and for packet authentication.
Support many programing languages.
Can run on numerous microcontroller/operating systems(including ARM7, ATMega, dsPic, STM32 and Windows, Linux, MacOS, Android and iOS).
Allows 255 systems on network.
Enables both offboard and onboard communications (e.g. between a GCS and UAV, and between UAV autopilot and MAVLink enabled UAV camera).

## Slide 16: Dronekit and Dronekit SITL
Bansilal Ramnath Agarwal Charitable Trust’s
Vishwakarma Institute of Information Technology
Department of Electronics & Telecommunication
It creates apps that can run on onboard companion computer and communicate with controller.
The API communicates with vehicles over MAVLink.
DroneKit Python APIs features:
    Connect to a vehicle (or multiple vehicles) from a script
    Get and set vehicle state/telemetry and parameter information.
    Receive asynchronous notification of state changes.
    Guide a UAV to specified position (GUIDED mode).
    Send arbitrary custom messages to control UAV movement and other hardware (GUIDED mode).
    Create and manage waypoint missions (AUTO mode).

## Slide 17: The SITL (software in the loop) simulator allows you to run Plane, Copter or Rover without any hardware. SITL Architecture:
Bansilal Ramnath Agarwal Charitable Trust’s
Vishwakarma Institute of Information Technology
Department of Electronics & Telecommunication

## Slide 18: ROS?
Bansilal Ramnath Agarwal Charitable Trust’s
Vishwakarma Institute of Information Technology
Department of Electronics & Telecommunication
ROS, the Robot Operating System, is an open source framework for getting robots to do things.
The Robot Operating System (ROS) is a framework for writing robot software. It is a collection of tools, libraries, and conventions that aim to simplify the task of creating complex and robust robot behavior across a wide variety of robotic platforms.

## Slide 19: Why to use ROS?
Bansilal Ramnath Agarwal Charitable Trust’s
Vishwakarma Institute of Information Technology
Department of Electronics & Telecommunication
The short answer is because it will save you time. ROS provides all the parts of a robot software system that you would otherwise have to write. It allows you to focus on the parts of the system that you care about, without worrying about the parts that you don’t care about.
Reliable
Uses TCPROS or UDPROS protocol for communication.

## Slide 20: Terms to understand for implementing ROS
Bansilal Ramnath Agarwal Charitable Trust’s
Vishwakarma Institute of Information Technology
Department of Electronics & Telecommunication
ROS Packages
ROS Nodes
ROS Topics
ROS Publisher(Python Script)
ROS Subscriber(Python Script)

## Slide 21: APPLICATION
Bansilal Ramnath Agarwal Charitable Trust’s
Vishwakarma Institute of Information Technology
Department of Electronics & Telecommunication
Search and rescue, forest fire monitoring and fighting, flood and earthquake response, etc.
First Aid delivery
Military observation of regions
Theatrical Performance
Building inspections - more drones, more coverage
Agriculture
This type of system can be use for surveillance on prohibited areas.

## Slide 22: REFERENCES
Bansilal Ramnath Agarwal Charitable Trust’s
Vishwakarma Institute of Information Technology
Department of Electronics & Telecommunication
https://www.theguardian.com/technology/2014/aug/15/harvard-kilobot-swarm-future-of-robotics[1]
https://pdfs.semanticscholar.org/645e/6080cee6d31fdda903809692ea6ab58b5990.[2]
https://www.researchgate.net/publication/264457775_Swarm_Intelligence_Concepts_Models_and_Applications[3]
https://www.hindawi.com/journals/isrn/2013/608164/[4]
http://www.techferry.com/articles/swarm-intelligence.html#aspects [5]
https://www.nrcresearchpress.com/journal/doi/10.1139/juvs-2018-0009?mobileUi=0#.XYLjUSgzbIV
https://www.thebalancecareers.com/military-and-civilian-drone-use-4121099
https://www.researchgate.net/publication/264457775_Swarm_Intelligence_Concept_Models_and_Applications
https://www.hindawi.com/journals/isrn/2013/608164/
https://www.sciencedirect.com/topics/agricultural-and-biological-sciences/swarms

## Slide 23: Thank You
Bansilal Ramnath Agarwal Charitable Trust’s
Vishwakarma Institute of Information Technology
Department of Electronics & Telecommunication